## Slide 1
ModelIt!
Student Lesson
Renewable Energy Grid Optimization: Powering the Future
Modeling the Complex Challenge of a 100 Percent Clean Energy Grid
NGSS: HS-PS3-3, HS-ETS1-3
9th Grade — Level 2: Advanced
1/9

## Slide 2
What You Will Learn Today
Learning Goals
* Model how intermittent renewable energy sources interact with grid demand, storage, and backup systems
* Analyze the optimization challenge of balancing cost, reliability, and emissions across an 8-component grid system
* Evaluate trade-offs between different energy mixes under varying demand and weather conditions
* Design a grid management strategy that achieves maximum renewable penetration while maintaining reliability
Key Vocabulary
Grid Intermittency
The variable and partially unpredictable nature of solar and wind energy production, which depends on weather rather than human control
Energy Storage
Technologies like batteries, pumped hydro, and hydrogen that store excess renewable energy for use when production is low
Dispatchable Generation
Power sources like natural gas or hydroelectric that can be turned on and off on demand to fill gaps in renewable production
Grid Balancing
The continuous process of matching electricity supply to demand in real time, which becomes more complex with intermittent sources
2/9

## Slide 3
The Big Question
Why can't we just replace all fossil fuel power plants with solar panels and wind turbines tomorrow?
Modeling the Complex Challenge of a 100 Percent Clean Energy Grid. Today we'll build a MODEL to discover the answer!
3/9

## Slide 4
Today We Will Build a Model!
A model helps us understand complex systems!
1. LOCATE
Identify the COMPONENTS (parts) of the system
2. ESTABLISH
Connect them with RELATIONSHIPS (+ or -)
3. VISUALIZE
Build your model in ModelIt!
4. EVALUATE
Run SIMULATIONS to test scenarios
5. REVISE
Improve your model based on evidence
4/9

## Slide 5
Activity 1: Sort the Components
Sort these components into EXTERNAL (inputs from outside) and INTERNAL (inside the system):
Your Components:
* Solar Output
* Wind Output
* Battery Storage
* Grid Demand
* Fossil Fuel Backup
* Transmission Efficiency
* Cost per kWh
* Carbon Emissions
Think: Which components can we control? Which happen on their own?
5/9

## Slide 6
Activity 2: Connect with Arrows
Draw arrows to show HOW components affect each other:
(+) POSITIVE Relationship
When one goes UP, the other goes UP too
(-) NEGATIVE Relationship
When one goes UP, the other goes DOWN
Think About It:
When Solar Output drops to zero at night and Wind Output is calm, how does Grid Demand get met? What happens to Cost per kWh when Battery Storage runs out and Fossil Fuel Backup kicks in? How do you minimize Carbon Emissions while keeping the lights on?
6/9

## Slide 7
Activity 3: Run the Simulation!
Test these scenarios in ModelIt!
Sunny Windy Day
Maximum solar and wind output -- observe how excess is stored and costs drop
Calm Winter Night
Zero solar, minimal wind -- observe battery depletion and fossil backup activation
Optimal Mix
Find the combination of solar, wind, storage, and backup that minimizes both cost and emissions
Watch the activity graphs change!
[ModelIt Platform Screenshot - Simulation Results Graph]
7/9

## Slide 8
What Did We Discover?
Our Model Showed Us:
* The last 10-20 percent of fossil fuel replacement is exponentially harder than the first 80 percent due to intermittency gaps
* Battery storage is essential but currently too expensive to cover multi-day renewable droughts without fossil backup
* Overbuilding renewable capacity to handle worst-case scenarios dramatically increases cost but reduces emissions
* Geographic diversity helps -- connecting solar-rich and wind-rich regions reduces the probability of system-wide intermittency
Answer: We cannot simply swap fossil plants for renewables because the sun and wind are intermittent -- they produce power when nature allows, not when humans need it. At night, on calm days, and during storms, renewable output drops to zero. Batteries can bridge short gaps but cannot economically cover multi-day droughts. Some fossil fuel backup remains necessary for reliability until storage technology improves dramatically. The optimization challenge is finding the mix of solar, wind, storage, and backup that minimizes cost AND emissions while keeping the grid reliable 99.97 percent of the time.
8/9

## Slide 9
STEM Challenge: Design a Regional Clean Energy Grid
YOUR ENGINEERING MISSION
Design the optimal energy mix for a region that achieves maximum renewable penetration while maintaining grid reliability and minimizing cost.
The Challenge:
A region of 5 million people must achieve 90 percent clean energy by 2035. Design the energy portfolio: how much solar, wind, storage, and backup do you need? What does it cost? How reliable is it during extreme weather?
Think Like an Engineer:
* What energy mix provides the best balance of cost, emissions, and reliability?
* How much battery storage is needed to bridge typical renewable gaps?
* What happens to your grid during a week-long cloudy calm period?
REAL CAREER CONNECTION: Grid Engineers and Energy Systems Analysts design and optimize electrical grids for the clean energy transition, earning $75,000-$140,000/year at utilities, grid operators, energy companies, and government agencies. The skills you're using TODAY are the same ones they use on the job!
9/9